## Slide 1: MULTI-ROBOT ROUTE FOLLOWING USING OMNIDIRECTIONAL VISION AND APPEARANCE-BASED REPRESENTATION OF THE ENVIRONMENT
L. Payá, O. Reinoso, A. Gil, J. Sogorb
MIGUEL HERNÁNDEZ UNIVERSITY INDUSTRIAL ENGINEERING SYSTEMS DEPARTMENT

## Slide 2: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 3: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 4: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 5: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 6: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 7: 1. Introduction
Presence of robots in our houses and factories is continuously increasing.
  Repetitive or unpleasant tasks.
To expand their range of home applications:
  Higher degree of autonomy, fulfilment and robustness.
EFFICIENT ENVIRONMENT REPRESENTATION
Variation in illumination
Occlusions
Change in the position of objects

## Slide 8: 1. Introduction
COMPLEX TASK
COLLABORATION BETWEEN A TEAM OF ROBOTS
The task is carried out quicker and in a more reliable way
ROUTE FOLLOWING
One robot following a leader one (formations problem).
Following a route that a previous robot has recorded.
Each robot works with incomplete and changing information.
  Representation of the environment.
  Communication between robots.
Complete knowledge of the environment.

## Slide 9: 1. Introduction
Main methods to carry out visual route following:
Model-based methods.
Appearance-based methods.

## Slide 10: 1. Introduction
Main methods to carry out visual route following:
Model-based methods.
Appearance-based methods.
Some features of the image are extracted to carry out localization and navigation.
Hard to use in non-structured environments.

## Slide 11: 1. Introduction
Main methods to carry out visual route following:
Model-based methods.
Appearance-based methods.
The scenes are stored with no feature extraction.
Recognition is achieved based on the matching of the whole images.
Problem with the size of the database and computational cost.

## Slide 12: 1. Introduction
Main methods to carry out visual route following:
Model-based methods.
Appearance-based methods.
Methods:
Direct comparison of low-resolution images.
Use of histogram and other global features.
Reduce previously the dimensionality of the data  PCA, Fourier…
Phases:
Learning phase: The robot stores general visual information from several points of view along the route.
Navigation phase: The robot follows the route comparing the current visual information with the stored one.

## Slide 13: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 14: 2. Representation of the environment
OBJECTIVE: Framework to carry out multi-robot route following using visual information and with an appearance-based approach.

## Slide 15: 2. Representation of the environment
64 x 256 images  Data vectors of 16384 elements.
   Generated with a 3 DOF process (Position and orientation of the robot).
Objective: Discard irrelevant or redundant data.
   PCA can be used for dimensionality reduction.

## Slide 16: 2. Representation of the environment
64 x 256 images  Data vectors of 16384 elements.
   Generated with a 3 DOF process (Position and orientation of the robot).
Objective: Discard irrelevant or redundant data.
   PCA can be used for dimensionality reduction.
SVD of the Covariance of the Data Matrix X
X = Data Matrix (M x N, N images x j, M pixels each image, M>>N), m is the mean image.
V = Matrix containing the K principal eigenvectors (computed from SVD of the Covariance Matrix).
P = Reduced (projected) data matrix. (K x N, K<N)

## Slide 17: 2. Representation of the environment
PCA database  All images of the route must be available before carrying out the compression.
  The robots to follow the route must wait the leader one finishes it.
  When a new image is added, the database must be built from the scratch.
Incremental PCA  Progressive construction of the database.
  Computationally expensive.
PCA is not invariant to rotation.

## Slide 18: 2. Representation of the environment
FOURIER TRANSFORM:
  Panoramic images can be transformed to another compact representation into the Fourier domain.
{an} = Initial sequence of complex numbers.
{An} = Transformed sequence of complex numbers.
Each row is transformed to the Fourier domain.

## Slide 19: 2. Representation of the environment
FOURIER TRANSFORM:
  When using omnidirectional images for localization:
    The most relevant information in the Fourier domain concentrates in the low frequency components.
    Rotational invariance.

## Slide 20: 2. Representation of the environment
FOURIER TRANSFORM:
  When using omnidirectional images for localization:
{an-q} = Shifted sequence (q = amount of shift).
Ak = Components of the Fourier transform of the non-shifted sequence.
    The most relevant information in the Fourier domain concentrates in the low frequency components.
    Rotational invariance.

## Slide 21: 2. Representation of the environment
FOURIER TRANSFORM:
  When using omnidirectional images for localization:
{an-q} = Shifted sequence (q = amount of shift).
Ak = Components of the Fourier transform of the non-shifted sequence.
    The most relevant information in the Fourier domain concentrates in the low frequency components.
    Rotational invariance.
Magnitude = 1.
Only phase change.

## Slide 22: 2. Representation of the environment
After the learning phase:
Original panoramic images
Fourier matrices (F < C)

## Slide 23: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 24: 3. Multi-Robot Route Following
LOCALIZATION OF THE FOLLOWER ROBOT:
  The follower robot captures an image and transforms it to the Fourier domain.
  The Fourier matrix is compared with the matrices in the database.
  The most similar point is the nearest position of the robot.
[t]i = Fourier matrix of the image captured by the follower robot.
[t]j = Fourier matrices stored in the database by the leader robot.

## Slide 25: 3. Multi-Robot Route Following
LOCALIZATION OF THE FOLLOWER ROBOT:
  The follower robot captures an image and transforms it to the Fourier domain.
  The Fourier matrix is compared with the matrices in the database.
  The most similar point is the nearest position of the robot.
APERTURE PROBLEM IN OFFICE ENVIRONMENTS.
  Probabilistic approach:
[t]i = Fourier matrix of the image captured by the follower robot.
[t]j = Fourier matrices stored in the database by the leader robot.
p(yj| [t]i;) is the probability of observing the Fourier Matrix [t]i if the position of the robot is yj.
p(yj) is the probability that the robot is on the position yj before observing the Fourier Matrix [t]i. This value is estimated using the information of the previous position and the motion model.
p([t]i|yj;) is the probability of observing [t]i if the position of the robot is yj. OBSERVATION MODEL.

## Slide 26: 3. Multi-Robot Route Following
OBSERVATION MODEL:
Sum of Gaussian kernels, centred on the n most similar points of the route.
Degree of similarity between the Fourier matrix of the currently captured image [t]i and the j-th Fourier matrix of the database.

## Slide 27: 3. Multi-Robot Route Following
OBSERVATION MODEL:
Sum of Gaussian kernels, centred on the n most similar points of the route.

## Slide 28: 3. Multi-Robot Route Following
CONTROL OF THE FOLLOWER ROBOT:
  Once the localization of the follower robot is known, its control action must be computed so that it tends to the route and follows it.
    The follower robot has to compute its orientation, comparing to the original heading that the leader robot had when it captured the image at that position.
  A method based on the extraction of some sub-windows along the panoramic images has been developed.
    Robust against small changes in illumination, partial occlusions and position of some objects in the environment.

## Slide 29: 3. Multi-Robot Route Following
CONTROL OF THE FOLLOWER ROBOT:
  Once the localization of the follower robot is known, its control action must be computed so that it tends to the route and follows it.
    The follower robot has to compute its orientation, comparing to the original heading that the leader robot had when it captured the image at that position.
  A method based on the extraction of some sub-windows along the panoramic images has been developed.
    Robust against small changes in illumination, partial occlusions and position of some objects in the environment.
A set of sub-images is obtained from the panoramic image the follower robot has just captured.

## Slide 30: 3. Multi-Robot Route Following
CONTROL OF THE FOLLOWER ROBOT:
  Once the localization of the follower robot is known, its control action must be computed so that it tends to the route and follows it.
    The follower robot has to compute its orientation, comparing to the original heading that the leader robot had when it captured the image at that position.
  A method based on the extraction of some sub-windows along the panoramic images has been developed.
    Robust against small changes in illumination, partial occlusions and position of some objects in the environment.
A set of sub-images is obtained on the corresponding image of the database.

## Slide 31: 3. Multi-Robot Route Following
CONTROL OF THE FOLLOWER ROBOT:
  Once the localization of the follower robot is known, its control action must be computed so that it tends to the route and follows it.
    The follower robot has to compute its orientation, comparing to the original heading that the leader robot had when it captured the image at that position.
  A method based on the extraction of some sub-windows along the panoramic images has been developed.
    Robust against small changes in illumination, partial occlusions and position of some objects in the environment.
The most similar sub-images in the corresponding image to the sub-images of the current image are extracted.

## Slide 32: 3. Multi-Robot Route Following
This information is arranged on a chart:
Several least square fittings are carried out in an iterative process where data are shifted before each new regression.
The orientation of the robot is proportional to the number of shifts until the best fitting is achieved.

## Slide 33: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 34: 4. Results
Processor C :
  Computes PCA subspace of the sub- windows.
  Computes the control action of Robot B.
Robot B:
  Captures a new image.
  Computes the Fourier matrix.
  Computes the nearest position.
  Sends to Processor C.
Robot A :
  Captures a new image.
  Transforms to panoramic view.
  Computes of the Fourier matrix.
  Sends to Processor C.

## Slide 35: 4. Results
  Route of around 50 meters.
  Recorded in an office environment.
  The follower robot moves forward only if its orientation is near to the right orientation.
  Second experiment. Initial orientation = 180º.
  Good performance on straight lines.
  Relatively bigger error on turnings.

## Slide 36: 4. Results
  Recovers from bad matchings.

## Slide 37: Contents
Introduction. Multi-robot systems and route following.
Representation of the environment.
  PCA.
  Fourier Transform.
Multi-robot route following.
  Localization of the robot.
  Control of the robot.
Results.
Conclusions.

## Slide 38: 5. Conclusions
The work presents a purely appearance-based multi-robot route following using low-resolution panoramic images of the environment and techniques of dimensionality reduction to extract the most relevant information from the scenes.
1D Fourier Transform  Invariability to rotation.
  Good for map building and localization.
PCA sub-images approach to compute the orientation.
The second robot can follow the route of the first one with a certain distance as in space or in time, localizing itself with respect to the route made by the first robot.
  Probabilistic algorithm to compute the position of the follower robot.
Some experiments have been carried out with two Pioneer 3-AT Robots using a CORBA-based architecture.

## Slide 39: MULTI-ROBOT ROUTE FOLLOWING USING OMNIDIRECTIONAL VISION AND APPEARANCE-BASED REPRESENTATION OF THE ENVIRONMENT
L. Payá, O. Reinoso, A. Gil, J. Sogorb
MIGUEL HERNÁNDEZ UNIVERSITY INDUSTRIAL ENGINEERING SYSTEMS DEPARTMENT